REALIZATION OF DIGITAL FILTERS
Mifta Nur Farid

---
INTRODUCTION

---
Introduction
- Basic steps to design of digital filters
  - Approximation
  - Realization
  - Study of arithmetic errors
  - Implementation

---
Approximation
- The process of generating a transfer function that would satisfy the desired speciﬁcations, which may concern the amplitude or phase response or even the time-domain response of the ﬁlter.
- Can be classiﬁed as direct or indirect.

---
Approximation
- In direct methods, the problem is solved directly in the z domain.
- In indirect methods, a continuous-time transfer function is ﬁrst obtained and then converted into a corresponding discrete-time transfer function.

---
Realization
- The process of generating a digital-ﬁlter network or structure from the transfer function or some other characterization of the ﬁlter.
- Can be classiﬁed as direct or indirect.
- In direct methods the realization is obtained directly from a given discrete-time transfer function
- In indirect realizations, the ﬁlter structure is obtained indirectly from an equivalent prototype analog ﬁlter.

---
Study of arithmetic errors
- During the approximation step, the coefﬁcients of the transfer function are determined to a high degree of precision.
- In practice, however, digital hardware have ﬁnite precision that depends on the length of registers used to store numbers; the type of number system used (e.g., signed-magnitude, two’s complement); the type of arithmetic used (e.g., ﬁxed-point or ﬂoating-point), and so on.

---
Study of arithmetic errors
- Consequently, ﬁlter coefﬁcients must be quantized (e.g., rounded or truncated) before they can be stored in registers.
- When the transfer function coefﬁcients are quantized, errors are introduced in the amplitude and phase responses of the ﬁlter, which are commonly referred to as quantization errors.

---
Study of arithmetic errors
Under these circumstances, the design process cannot be deemed to be complete until the effects of arithmetic errors on the performance of the ﬁlter are investigated and ways are found to mitigate any problems associated with numerical imprecision.

---
Implementation
- Implementation of a digital ﬁlter can assume two forms, namely, software or hardware.
- Software: implementation involves the simulation of the ﬁlter network on a general-purpose digital computer, workstation, or DSP chip.
- Hardware: it involves the conversion of the ﬁlter network into a dedicated piece of hardware.

---
Implementation
- In nonreal-time applications where a record of the data to be processed is available, a software implementation may be entirely satisfactory.
- In real-time applications, however, where data must be processed at a very high rate (e.g., in communication systems), a hardware implementation is mandatory.

---
Realization
- The natural order of the four basic design steps is as stated in the preceding discussion, namely, approximation, realization, study of imperfections, and implementation.
- However, realization is that much easier to learn than the approximation process and for this reason it will be treated ﬁrst.

---
REALIZATION

---
Realization
- The most frequently used direct realization methods of this class are
  - Direct
  - Direct canonic
  - State-space
  - Lattice
  - Parallel
  - Cascade

---
DIRECT REALIZATION

---
Realization
In indirect methods, on the other hand, a given analog-ﬁlter network is represented by the so-called wave characterization, which is normally used to represent microwave circuits and systems, and through the use of a certain transformation the analog-ﬁlter network is converted into a topologically related digital-ﬁlter network

---
Direct Realization
A ﬁlter characterized by the N th-order transfer function

---
Direct Realization

---
Direct Realization

---
Direct Realization

---
Direct Realization

---
Direct Realization

---
Direct Realization

---
Direct Realization

---
Direct Realization

---
Direct Realization
- The above cycle of activities can be repeated N times whereupon NN(z) will reduce to a single multiplier.
- In each cycle of the procedure there are two possibilities, and since there are N cycles, a total of 2N distinct networks can be deduced for N(z).

---
Direct Realization

---
Direct Realization

---
Direct Realization

---
Direct Realization

---
Direct Realization

---
Example 1
Realize the transfer function

---
DIRECT CANONIC REALIZATION

---
Direct Canonic Realization
- The smallest number of unit delays required to realize an N th-order transfer function is N.
- An N th-order discrete-time network that employs just N unit delays is said to be canonic with respect to the number of unit delays.

---
Direct Canonic Realization

---
Direct Canonic Realization

---
Direct Canonic Realization

---
Direct Canonic Realization

---
STATE-SPACE REALIZATION

---
State-Space Realization
Another approach to the realization of digital ﬁlters is to start with the state-space characterization

---
State-Space Realization
Another approach to the realization of digital ﬁlters is to start with the state-space characterization

---
State-Space Realization
For an N th-order ﬁlter

---
State-Space Realization
state-space signal ﬂow graph

---
Example 2
A digital ﬁlter is characterized by the state-space equations
Obtain a direct canonic realization.

---
LATTICE REALIZATION

---
Lattice Realization

---
Lattice Realization
The realization can be accomplished by using a recursive algorithm comprising N iterations whereby polynomials of the form
are generated for j = N , N − 1, . . . , 0, and for each value of j the multiplier constants νj and µj are evaluated using coefﬁcients αjj and βjj in the above polynomials

---
Lattice Realization

---
Lattice Realization

---
Lattice Realization

---
Lattice Realization

---
Example 3
Realize the transfer function’
using the lattice method

---
Lattice Realization
- The 2-multiplier section yields structures that are canonic with respect to the number of unit delays.
- However, the number of multipliers can be quite large, as can be seen in Example 3.

---
Lattice Realization
More economical realizations can be obtained by using 1-multiplier ﬁrst-order sections of the type shown below

---
Lattice Realization
- Such realizations can be obtained by ﬁrst realizing the transfer function in terms of 2-multiplier sections as described above and then replacing each of the 2-multiplier sections by either of the 1-multiplier sections
- The denominator multiplier constants µ1, µ2, . . . , µN remain the same as before. However, the numerator multiplier constants ν0, ν1, . . . , νN must be modiﬁed as

---
Lattice Realization
Each parameter εi is a constant which is equal to +1 or −1 depending on whether the ith 2-multiplier section is replaced by the 1-multiplier section of Fig. a or that of Fig. b.

---
CASCADE REALIZATION

---
Cascade Realization
- When the transfer function coefﬁcients are quantized, errors are introduced in the amplitude and phase responses of the ﬁlter.
- When a transfer function is realized directly in terms of a single N th-order network using any one of the methods described so far, the sensitivity of the structure to coefﬁcient quantization increases rapidly with N
- Consequently, small errors introduced by coefﬁcient quantization give rise to large errors in the amplitude and phase responses.

---
Cascade Realization
- This problem can to some extent be overcome by realizing high-order ﬁlters as interconnections of ﬁrst- and second-order networks.
- In this and the next section, it is shown that an arbitrary transfer function can be realized by connecting a number of ﬁrst- and second-order structures in cascade or in parallel.

---
Cascade Realization
Consider an arbitrary number of ﬁlter sections connected in cascade as
and assume that the ith section is characterized by

---
Cascade Realization

---
Cascade Realization
The overall transfer function of a cascade arrangement of ﬁlter sections is equal to the product of the individual transfer functions, that is,
An N th-order transfer function can be factorized into a product of ﬁrst- and second-order transfer functions of the form

---
Example 4
Obtain a cascade realization of the transfer function
using canonic sections.

---
PARALLEL REALIZATION

---
Parallel Realization
Another realization comprising ﬁrst- and second-order ﬁlter sections is based on the parallel conﬁguration

---
Parallel Realization

---
Example 5
Obtain a parallel realization of the transfer function
using canonic sections.